Page 1/2

IEC 61850 Certificate Level A/B1

| <UCAIUG logo> | No. -xxxx |
| --- | --- |
| Issued to: | For the client system: |
| <<MANUFACTURER>> <<FULL ADDRESS>> | <<CLIENT NAME>> <<VERSION NUMBER>> <<ADDITIONAL INFO>> |

Issued by: <TESTLAB>

# The client system has not shown to be non-conforming to:

## IEC 61850-6, 7-1, 7-2, 7-3, 7-4 and 8-1

### Communication networks and systems in substations

The conformance test has been performed according to IEC 61850-10 and UCA IUG Conformance Test Procedures for Client System with IEC 61850-8-1 interface, revision 1.1 with TPCL version 1.2 with client system’s protocol, model and technical issue implementation conformance statements: “<<PICS>>”, “<<MICS>>”, “<<TICS>>” and product’s extra information for testing: “<<PIXIT>>”.

The following IEC 61850 conformance blocks have been tested with a positive result (number of relevant and executed test cases / total number of test cases):

| 1 Basic Exchange (../22) 2 Data Sets (../9) 2+ Data Set Definition (../4) 3 Substitution (../3) Setting Group Selection (../4) 4+ Setting Group Definition (../2) Unbuffered Reporting (../18) Buffered Reporting (../22) | 12a Direct Control (../7) 12b SBO Control (../9) 12c Enhanced Direct Control (../7) 12d Enhanced SBO Control (../9) 13 Time Synchronization (../4) 14 File Transfer (../8) |
| --- | --- |

This certificate includes a summary of the test results as carried out at <testlab> in the <country> with <IED SIMULATOR> and <ANALYZER>. This document has been issued for information purposes only, and the original paper copy of the test report: No. xxxx will prevail.

<<LOCATION, DATE>>

<<manager NAME>>	<<NAME>>

<<JOB TITLE>>	<<JOB TITLE>>

# 1 Level A - Independent Test lab with certified ISO 9000 or ISO 17025 Quality System

# Level B – Recognized Test lab with ISO 9000 or ISO 17025 equivalent Quality System

# 2 TPCL – test procedure change list

Page 2/2

Applicable Test Procedures from the UCA IUG Conformance Test Procedures for Client System with IEC 61850-8-1 interface, revision 1.1 with TPCL version 1.2

| Conformance Block | Mandatory | Conditional |
| --- | --- | --- |
| 1: Basic Exchange | cAss1, cAss2, cAss3, cAss4, cAssN1, cAssN4, cAssN5, cAssN6 | cAssN7 cSrv1, cSrv2, cSrv3, cSrv4, cSrv5, cSrv6, cSrv7, cSrvN1, cSrvN2, cSrvN3, cSrvN4, cSrvN5, cSrvN6 |
| 2: Data Sets |  | cDs1, cDs2, cDs3, cDs4, cDs5, cDsN1a, cDsN1b, cDsN2, cDsN3 |
| 2+: Data Set Definition | cDs6, cDsN4 | cDs7, cDsN5 |
| 3: Substitution | cSub1 | cSub2, cSub3 |
| 4: Setting Group Selection | cSg2, cSgN1 | cSg1, cSg3 |
| 4+: Setting Group Definition | cSg3, cSg4 |  |
| 5: Unbuffered Reporting | cRp3, cRp4, cRp5, cRp8, cRp9, cRp10, cRpN2, cRpN3, cRpN7, cRpN8 | cRp1, cRp2, cRp6, cRp7, cRpN1, cRpN4, cRpN5, cRpN6 |
| 6: Buffered Reporting | cBr3, cBr4, cBr5, cBr8, cBr9, cBr10, cBr11, cBr12, cBrN2, cBrN3, cBrN7, cBrN8, cBrN9 | cBr1, cBr2, cBrN1 cBr6, cBr7, cBr13, cBrN4, cBrN5, cBrN6 |
| 12a: Direct control | cCtl4, cCtlN1 cDOns1, cDOns2 | cCtl1, cCtl2, cCtl3 |
| 12b: SBO control | cCtl4, cCtlN1 cSBOns1, cSBOns2, cSBOns3 | cCtl1, cCtl2, cCtl3, cSBOns4 |
| 12c: Enhanced Direct Control | cCtl4, cCtlN1 cDOes1, cDOes2 | cCtl1, cCtl2, cCtl3 |
| 12d: Enhanced SBO control | cCtl4, cCtlN1, cSBOes1, cSBOes2, cSBOes3 | cCtl1, cCtl2, cCtl3 cSBOes4 |
| 13: Time sync | cTm1 | cTm2, cTmN1, cTmN2 |
| 14: File transfer | cFt1, cFt2, cFt3, cFtN1, cFtN2 | cFt4, cFt5, cFtN3 |