Protocol Implementation eXtra Information for Testing (PIXIT)

for the IEC 61850 interface in <device>

UCA International Users Group

Testing Sub Committee

Template version 1.1

Date: March 20, 2008

# Introduction

This document specifies the protocol implementation extra information for testing (PIXIT) of the IEC 61850 interface in <device> with firmware version <version>.

Together with the PICS and the MICS the PIXIT forms the basis for a conformance test according to IEC 61850-10.

## Contents of this document

Each chapter specifies the PIXIT for each applicable ACSI service model as structured in IEC 61850-10.

# PIXIT for Association model

| Description | Value / Clarification |
| --- | --- |
| Maximum number of clients that can set-up an association simultaneously | … |
| TCP_KEEPALIVE value | … seconds |
| Lost connection detection time | … seconds |
| Is authentication supported | Y/N |
| What association parameters are necessary for successful association | Transport selector Y/N Session selector Y/N Presentation selector Y/N AP Title Y/N AE Qualifier Y/N |
| If association parameters are necessary for association, describe the correct values e.g. | Transport selector 0001 Session selector 0001 Presentation selector 00000001 AP Title na AE Qualifier na |
| What is the maximum and minimum MMS PDU size | Max MMS PDU size … Min MMS PDU size … |
| What is the maximum startup time after a power supply interrupt | … seconds |
| <additional items> |  |

# PIXIT for Server model

| Description | Value / Clarification |
| --- | --- |
| Which analogue value (MX) quality bits are supported (can be set by server) | Validity: Y/N Good, Y/N Invalid, Y/N Reserved, Y/N Questionable Y/N Overflow Y/N OutofRange Y/N BadReference Y/N Oscillatory Y/N Failure Y/N OldData Y/N Inconsistent Y/N Inaccurate Source: Y/N Process Y/N Substituted Y/N Test Y/N OperatorBlocked |
| Which status value (ST) quality bits are supported (can be set by server) | Validity: Y/N Good, Y/N Invalid, Y/N Reserved, Y/N Questionable Y/N BadReference Y/N Oscillatory Y/N Failure Y/N OldData Y/N Inconsistent Y/N Inaccurate Source: Y/N Process Y/N Substituted Y/N Test Y/N OperatorBlocked |
| What is the maximum number of data values in one GetDataValues request |  |
| What is the maximum number of data values in one SetDataValues request |  |
| <additional items> |  |

# PIXIT for Data set model

| Description | Value / Clarification |
| --- | --- |
| What is the maximum number of data elements in one data set (compare ICD setting) |  |
| How many persistent data sets can be created by one or more clients |  |
| How many non-persistent data sets can be created by one or more clients |  |
| <additional items> |  |

# PIXIT for Substitution model

| Description | Value / Clarification |
| --- | --- |
| <additional items> |  |

# PIXIT for Setting group control model

| Description | Value / Clarification |
| --- | --- |
| What is the number of supported setting groups for each logical device (compare NumSG in the SGCB) |  |
| What is the effect of when and how the non-volatile storage is updated (compare IEC 61850-8-1 $16.2.4) |  |
| Can multiple clients edit the same setting group | Y/N |
| What happens if the association is lost while editing a setting group | Y/N |
| Is EditSG value 0 allowed? | Y/N |
| <additional items> |  |

# PIXIT for Reporting model

| Description | Value / Clarification |
| --- | --- |
| The supported trigger conditions are (compare PICS) | integrity Y/N data change Y/N quality change Y/N data update Y/N general interrogation Y/N |
| The supported optional fields are | sequence-number Y/N report-time-stamp Y/N reason-for-inclusion Y/N data-set-name Y/N data-reference Y/N buffer-overflow Y/N entryID Y/N conf-rev Y/N segmentation Y/N |
| Can the server send segmented reports | Y/N |
| Mechanism on second internal data change notification of the same analogue data value within buffer period (Compare IEC 61850-7-2 $14.2.2.9) | Send report immediately OR Replace analogue value in pending report |
| Multi client URCB approach (compare IEC 61850-7-2 $14.2.1) | Each URCB is visible to one client only or Each URCB is visible to all clients |
| What is the format of EntryID |  |
| What is the buffer size for each BRCB or how many reports can be buffered |  |
| Pre-configured RCB attributes that cannot be changed online when RptEna = FALSE (see also the ICD report settings) |  |
| May the reported data set contain: - structured data objects? - data attributes? - timestamp data attributes? | Y/N Y/N Y/N, will/will not be included in a dchg report |
| What is the scan cycle for binary events? Is this fixed, configurable | …. Mseconds Fixed or Configurable |
| <additional items> |  |

# PIXIT for Logging model

| Description | Value / Clarification |
| --- | --- |
| What is the default value of LogEna (Compare IEC 61850-8-1 $17.3.3.2.1, the default value should be FALSE) | TRUE/FALSE |
| What is the format of EntryID (Compare IEC 61850-8-1 $17.3.3.3.1) |  |
| If there are multiple Log Control Blocks that specify the Journaling of the same MMS NamedVariable and TrgOps and the Event Condition (Compare IEC 61850-8-1 $17.3.3.3.2) | Single Journal Entry (specify the event condition) or Multiple Journal Entries |
| Pre-configured LCB attributes that cannot be changed online |  |
| <additional items> |  |

# PIXIT for Generic substation events model

| Description | Value / Clarification |
| --- | --- |
| What elements of a subscribed GOOSE header are checked to decide the message is valid and the allData values are accepted? If yes, describe the conditions. Note: the VLAN tag may be removed by a ethernet switch and should not be checked | Y/N source MAC address Y/N destination MAC address Y Ethertype = 0x88B8 Y/N gocbRef Y/N timeAllowedtoLive Y/N datSet Y/N goID Y/N t Y/N stNum Y/N sqNum Y/N test Y/N confRev Y/N ndsCom Y/N numDatSetEntries |
| Can the test flag in the published GOOSE be turned on / off | Y/N |
| What is the behavior when the GOOSE publish configuration is incorrect | DUT will send GOOSE with NdsCom=T or DUT keeps GoEna=F |
| When is a subscribed GOOSE marked as lost? (TAL = time allowed to live value from the last received GOOSE message) | a) message does not arrive prior to TAL b) message does not arrive by 2x TAL c) message does not arrive by TAL plus configurable time d) other (describe) |
| What is the behavior when one or more subscribed GOOSE messages isn’t received or syntactically incorrect (missing GOOSE) |  |
| What is the behavior when a subscribed GOOSE message is out-of-order |  |
| What is the behavior when a subscribed GOOSE message is duplicated |  |
| Does the device subscribe to GOOSE messages with/without the VLAN tag? | Y/N, with the VLAN tag Y/N, without the VLAN tag |
| May the GOOSE data set contain: - structured data objects? - data attributes? - timestamp data attributes? | Subscribed Published Y/N Y/N Y/N Y/N Y/N Y/N |
| What is the slow retransmission time? Is it fixed or configurable? | … mseconds with TAL = … Fixed or Configured by …. |
| What is the fast retransmission scheme? Is it fixed or configurable? | 1) … mseconds with TAL = … 2) … mseconds with TAL = … 3) … mseconds with TAL = … 4) … mseconds with TAL = … 5) … mseconds with TAL = … 6) … mseconds with TAL = … Fixed or Configured by …. |
| Can the Goose publish be turned on / off by using SetGoCBValues(GoEna) | Y/N |
| <additional items> |  |

TAL = Time Allowed to Live

# PIXIT for Control model

| Description | Value / Clarification |
| --- | --- |
| What control modes are supported (compare PICS) | Y/N status-only Y/N direct-with-normal-security Y/N sbo-with-normal-security Y/N direct-with-enhanced-security Y/N sbo-with-enhanced-security |
| Is the control model fixed, configurable and/or online changeable? | Fixed / Configurable / Online changeable |
| Is Time activated operate (operTm) supported | Y/N |
| Is “operate-many” supported | Y/N |
| What is the behavior of the DUT when the test attribute is set in the SelectWithValue and/or Operate request | e.g. DUT ignores the test value and execute the command as usual |
| What are the conditions for the time (T) attribute in the SelectWithValue and/or Operate request | e.g. DUT ignores the time value and execute the command as usual |
| Is pulse configuration supported | Y/N |
| What is the behavior of the DUT when the check conditions are set Is this behavior fixed, configurable, online changeable? | Y/N synchrocheck Y/N interlock-check DUT ignores the check value and always perform the check or DUT uses the check value to perform the check or not Fixed / Configurable / Online changeable |
| What additional cause diagnosis are supported | Y/N Blocked-by-switching-hierarchy Y/N Select-failed Y/N Invalid-position Y/N Position-reached Y/N Parameter-change-in-execution Y/N Step-limit Y/N Blocked-by-Mode Y/N Blocked-by-process Y/N Blocked-by-interlocking Y/N Blocked-by-synchrocheck Y/N Command-already-in-execution Y/N Blocked-by-health Y/N 1-of-n-control Y/N Abortion-by-cancel Y/N Time-limit-over Y/N Abortion-by-trip |
| How to force a “test-not-ok” respond with SelectWithValue request? |  |
| How to force a “test-not-ok” respond with Select request? |  |
| How to force a “test-not-ok” respond with Operate request? | DOns: SBOns: DOes: SBOes: |
| Which origin categories are supported? |  |
| What happens if the orCat is not supported? | DOns: SBOns: DOes: SBOes: |
| Does the IED accept an selectwithvalue/operate with the same ctlVal as the current status value? | DOns: Y/N SBOns: Y/N DOes: Y/N SBOes: Y/N |
| Does the IED accept a select/operate on the same control object from 2 different clients at the same time? | DOns: Y/N SBOns: Y/N DOes: Y/N SBOes: Y/N |
| Does the IED accept a select/selectwithvalue from the same client when the control object is already selected (tissue 334) | SBOns: Y/N SBOes: Y/N |
| Is for SBOes the internal validation performed during the SelectWithValue and/or Operate step? | SelectWithValue / Operate / SelectWithValue and Operate |
| Can a control operation be blocked by Mod=Off or Blocked | Y/N |
| Does the IED support local / remote operation? | Y/N |
| <additional items> |  |

# PIXIT for Time and time synchronisation model

| Description | Value / Clarification |
| --- | --- |
| What quality bits are supported? | Y/N LeapSecondsKnown Y/N ClockFailure Y/N ClockNotSynchronized |
| Describe the behavior of the IED when the time synchronization signal/messages are lost |  |
| When is the time quality bit "Clock failure" set? | Compare comment 3, 4 and 5 |
| When is the time quality bit "Clock not synchronised” set? | Compare comment 6 |
| Is the timestamp of a binary event adjusted to the configured scan cycle? | Y/N |
| Does the device support time zone and daylight saving? | Y/N |
| Which attibutes of the SNTP response packet are validated? | Y/N Leap indicator not equal to 3? Y/N Mode is equal to SERVER Y/N OriginateTimestamp is equal to value sent by the SNTP client as Transmit Timestamp Y/N RX/TX timestamp fields are checked for reasonableness Y/N SNTP version 3 and/or 4 Y/N other (describe) |
| <additional items> |  |

# PIXIT for File transfer model

| Description | Value / Clarification |
| --- | --- |
| What is structure of files and directories? |  |
| Is the IETF FTP protocol also implemented |  |
| Directory names are separated from the file name by | “/” or “\” |
| The maximum file name size including path (recommended 64 chars) | … chars |
| Are directory/file name case sensitive | Case sensitive |
| Maximum file size |  |
| Is the requested file path included in the file name of the MMS fileDirectory respond? | Y/N |
| Is the wild char supported MMS fileDirectory request? | Yes, wild card = * and/or *.* No |
| Is it allowed that 2 client get a file at the same time? | Y/N |
| <additional items> |  |

Instruction and comments on using this template

Comments

- The template is updated according to the PIXIT references in the server conformance test procedures version 2.2

- Questions and comments can be e-mailed to: helpdesk@ucausersgroup.org

- The non-use of the 7-2 mandatory “ClockFailure” will be allowed. However, this will be changed in the future to require full compliance with IEC 61850 Part 7-2

- According to IEC 61850-7-2 $5.5.3.7.3.3 clock failure is mandatory and shall indicate that the time source of the sending device is unreliable.

- Devices are prohibited from exposing the semantic ClockFailure using anything other than the ClockFailure bit

- According to IEC 61850-7-2 $5.5.3.7.3.3 clock not synchronised is optional and shall indicate that the time source of the sending device is not synchronized with the external UTC time

Instructions

- format of the document may be changed into your company format

- enter the applicable IED name and firmware version

- remove the non-applicable clauses

- remove the <additional items> row

- add new rows when/where applicable to describe additional functionality important for testing

Revision history

| Revision | Remarks |
| --- | --- |
| 0.1 | First version of the UCAIUG template |
| 1.0 | Clarified - reporting of Timestamp data attributes Clarified GOOSE subscribtion lost detection Added GOOSE publish transmission scheme |
| 1.1 | Clarify the handling of Clock Failure as follows added comment: The non-use of the 7-2 mandatory “ClockFailure” will be allowed. However, this will be changed in the future to require full compliance with IEC 61850 Part 7-2 Added comment: devices are prohibited from exposing the semantic ClockFailure using anything other than the ClockFailure Bit. This prohibits a vendor from always sending ClockFailure=FALSE while setting some alternate bit elsewhere to indicate that the clock has failed |