IEC 61850 Merging Unit Publisher Certificate Template

UCA-QMF-070

Review History

| Date | Reviewer | Comments |
| --- | --- | --- |
| 03/02/11 | BAM | Initial release |

IEC 61850 Merging Unit Conformance Certificate Requirements

Each certificate shall include at least the following information:

a) a title (e.g. "IEC 61850 Test Certificate");

b) the name and address of the test center, and the location where the tests were carried out, if different from the address of the test center;

c) unique identification of the certificate (such as the serial number), and on each page an identification in order to ensure that the page is recognized as a part of the certificate;

d) the name and address of the client;

e) identification of the method used;

f) a description of, the condition of, and unambiguous identification of the test system (hardware, firmware, software level) and the devices and item(s) tested;

g) the date of receipt of the test item(s) where this is critical to the validity and application of the results, and the date(s) of performance of the test;

h) reference to the standards and procedures (including version number) used by the test center or other bodies where these are relevant to the validity or application of the results;

i) the test results with the specification of conformance blocks;

j) the name(s), function(s) and signature(s) or equivalent identification of person(s) authorizing the certificate;

k) where relevant, a statement to the effect that the results relate only to the items tested.

NOTE 1 Hard copies of test reports and  certificates should also include the page number and total number of pages.

NOTE 2 It is recommended that test centers include a statement specifying that the test report or certificate shall not be reproduced except in full, without written approval of the test center.

EXAMPLE Certificate

IEC 61850 Certificate Level A/B

Page 1 of 2

No. XYZ

Tested by: 	For the 92LE publisher:

<Testlab>		<Name of Product>

<Hardware version>

Issued to:	<Firmware version>

<Name of Company> 	Supporting:

<Address of Company> 	1/3/4 phase voltage and current

Neutral is <calculated><measured>

Serial nr.: ........

The product has not shown to be non-conforming to:

IEC 61850-6, 7-2 and 9-2

Communication networks and systems in substations.

The conformance test has been performed according to IEC 61850-10 with 92LE publisher’s protocol implementation conformance statement: “<PICS PIXIT>” and extra information for testing: “<PIXIT>”.

The following IEC 61850 conformance blocks have been tested with a positive result (number of relevant and executed test cases / total number of test cases as defined in the UCAIUG Test procedures for Sampled Values Publishers according to the "Implementation Guideline for Digital Interface to Instrument Transformers using IEC 61850-9-2" (9-2LE), version 1.1):

| 11a Sampled Value publish (13/17) | 50 Hz with 80 samples per cycle |
| --- | --- |
| 11a Sampled Value publish (13/17) | 60 Hz with 80 samples per cycle |
| 11a Sampled Value publish (13/17) | 50 Hz with 256 samples per cycle |
| 11a Sampled Value publish (13/17) | 60 Hz with 256 samples per cycle |

This Certificate includes a summary of the test results as carried out at <location> with <Analyzer version>. The test is based on the UCAIUG “Test procedures for Sampled Values Publishers according to the "Implementation Guideline for Digital Interface to Instrument Transformers using IEC 61850-9-2" (9-2LE), version 1.1”. This document has been issued for information purposes only, and the original paper copy of the test report: No. <document reference> will prevail.

The test has been carried out on one single specimen of the client system as referred above and submitted to <testlab> by <manufacturer>. The manufacturer’s production process has not been assessed. This Certificate does not imply that <testlab> has certified or approved any product other than the specimen tested.

<Location & date>

<manager name>	<name>

<tiltle>	<Test Engineer>

Page 2 of 2

Applicable Test Procedures from the UCAIUG "Test procedures for Sampled Values Publishers according to the "Implementation Guideline for Digital Interface to Instrument Transformers using IEC 61850-9-2 (9-2LE)", version 1.1”

| Conformance Block | Mandatory | Conditional |
| --- | --- | --- |
| Configuration | Cnf1, Cnf2, Cnf3, Cnf4, Cnf5, Cnf6, Cnf7, Cnf8 | Cnf9 |
| 11a Sampled Value Publishing 50 Hz, 80 samples/cycle | Svp1, Svp2, Svp3, Svp6, Svp10, Svp11, Svp14, Svp15 | Svp4, Svp7, Svp8, Svp16, Svp17 |
| 11a Sampled Value Publishing 60Hz, 80 samples/cycle | Svp1, Svp2, Svp3, Svp6, Svp10, Svp11, Svp14, Svp15 | Svp4, Svp7, Svp8, Svp16, Svp17 |

<This area is used for notes from the tester or certification body>

# Footnotes

Level  A – Independent Tester with certified ISO 9000 or ISO 17025 Quality System

Level  B – Tester with ISO 9000 or ISO 17025 Quality System