Outline of Test Procedure for 61850-90-5 Clients and Servers

- Static conformance

  - PICS

  - MICS

  - PIXIT

  - TICS

  - Declaration as server

  - Declaration as client

  - Declaration as PDC (is this different?)

- Object Model checks

  - Basic LD with LPHD1, LLN0, {MMXUn or MSQIn}

  - Dataset declaration for GOOSE and/or SV

  - Control Blocks for RS and RG (R-MSVCB or R-GOCB, etc.)

- Communications

  - Ensure cyclic data sent as SV, acyclic as GOOSE (specifically, cyclic cannot be GOOSE)

  - UDP and/or TCP support (is there another type of tunneling?)

  - IPv4 and/or IPv6

- SCL file usage

  - Server -> ICD -> Client

  - Server -> IID -> Client

  - Server (( SED (( Client

  - CID -> Server or Client

- Performance

  - Supported cyclic rates (1,2,3,4,5,6,10,15,20,30,60,120,240) {is this the right list?)

  - HSR and/or PRP

  - Filtering/accuracy class: M (metering) or P (Protection)

Open questions:

- Should test procedure be structured similarly to 61850-8-1 server and client?

- Are there items in the list which present challenges for testing (ISO connectionless transport scares me because it was part of GSSE)

- What should PICS include? I think we should minimize PIXIT to be only for testing (“how do you cause a device to emit a …”)

- Are there functional states to check (Mod, Beh)

- What about test bits (for example, the GOOSE simulation bit)?