Comments Form, please mail to Richard.Schimmel@kema.com

Results from the tele conference March 3

| Date | Document |
| --- | --- |
| March 4, 2008 | Conformance Test Procedures for Client Devices with IEC 61850-8-1 interface Revison 0.8 |

| Comment Author | Clause/ Subclause | Paragraph Figure/ Table | COMMENTS | Proposed change | OBSERVATIONS OF THE Testsub comittee |
| --- | --- | --- | --- | --- | --- |
| SISCO-A1 | A.4 | Table A.4.2 | For Substition, C_Sub3 needs to be added (see clause A.4.3) | Add C_Sub3 as conditional upon execution of C_Sub2 | Agree DONE |
| SISCO –A2 | A.4.3 | C_Sub1 | Detailed Test cases for C_Sub1 and C_Sub2 are incorrect | Update per the agreed upon text from Previoous SISCO27 comment: 1. Make precondition of test support for GetDataValues. 2. State for each SV is a single Server. 3. Change test description to be: DUT sets a substituted value DUT enables substitution Server verifies that substation is correct. DUT disables substitution. Server verifies that disable is correct. 4. If reporting/quality display is desired, add an additional test case. | Compare annex A typical gateway has no display features. Change “display” into “process” in the document. DONE |
| SISCO-A3 | A.4.4 |  | Previously Submitted SISCO28 is still open pending tissue resolution. |  | Wait for tissue #593 |
| SISCO-A4 | general |  | Clause A.4.8 is missing, | Should have a section labled intentionally left blank. | NOT agree, GSSE is out-of-scope, server also does not have GSSE testprocedures No change |
| SISCO-A5 |  | C_Ctl3 | Test description calls out use of PIXIT but actual test procedure does not (old SISCO84) | Add PIXIT to detailed test procedure. | Agree DONE |
| SISCO-A6 |  | C_DOns3 | There is no detailed test procedure present. |  | Detailed test procedures exclude TimeActivatedOperate test cases: DOns3-4-5 No change |
| SISCO-A7 |  | C_SBOns1 | PIXIT use was not added as agreed upon (old SISCO92) | Update to add reference to use of PIXIT in description and detailed test. | Agree, compare annex DONE |
| SISCO-A8 |  | C_SBOns2 | PIXIT use was not added as agreed upon (old SISCO93) | Update to add reference to use of PIXIT in description and detailed test. | NOT agree, this is the normal operation No change |
| SISCO-A9 |  | C_DOes1 | SISCO old comment (SISCO100) was not implemented as agreed upon. | Update to add reference to use of PIXIT in description and detailed test. | Agree, see annex DONE |
| SISCO-A10 |  | C_DOes2 | SISCO old comment (SISCO101) was not implemented as agreed upon. | Update to add reference to use of PIXIT in description and detailed test. | Agree, see annex DONE |
| SISCO-A11 |  | C_DOes3 C_DOes4 | There are no detailed test procedures for these tests. Additonally, the old SISCO comments (SISCO102/103) were not reflected (e.g. the test descriptions did not mention PIXIT). | Either create the detailed tests procedures or label them as out-of-scope for the current document. Update test description to reference PIXIT. | Detailed test procedures exclude TimeActivatedOperate test cases: DOes3-4 No change |
| SISCO-A12 |  | C_Ft4 | The previously agreed upon comment (SISCO119) was not implement. | Add PIXIT information to detailed test description. | Agree, see annex DONE |
| SISCO-A13 |  | C-FtN1 Table A.4.2 | Old SISCO comment (SISCO120) was not implement as agreed upon. | Make C_FtN1 optional. | Split conformance block 14: 14a = GetServerDirectory(FILE), GetFileAttributes, GetFile 14b = SetFile DONE At the telco we proposed to rename Annex A into “Detailed MMS Test procedures and results”, and move GOOSE to new annex B: “Detailed GOOSE Test procedures and results”. It is more logical to change: A4 and add A5: A4. Mapping on MMS (IEC 61850-7-2 and IEC 61850-8-1) A5. Mapping of GOOSE (IEC 61850-7-2 and IEC 61850-8-1) DONE Because A1= Documentation, A2= Configuration, A3= datamodelling A1-A2-A3-A4-A5 need to visible in the contents page DONE |
| SISCO-A14 |  | C_SrvN1 C_SrvN2 C_SrvN3 C_SrvN4 C_DsN1 | Text describing the expected results uses the word indicates which could be interpreted as each negative response must be pointed out, stated, or expressed to a user. | Change the text from indicates to receives | Change “indicates” to “process” SEE ANNEX DONE |
| SISCO-A15 |  | C-SrvN1 | Text in test descriptions 4,5,6 uses unknown. Note that after the server is reconfigured in step 2 the logical device, logical node and data object no longer exist. If it has to be an unknown or non-existant ObjectName any name value will satisfy the test input. | Change the text from unknown to previously known. | Agree SEE ANNEX DONE |
| SISCO-A16 |  | C_SrvN1 | Test description 7, 8 Getting a Data Definition of a known data object in either case will produce a DataDefinition response not a negative response( the negative response for GetDataDefinition is test 6) | Change the expected results for 7 8 to SUT receives a GetDataDefinition response and continues as specified in PIXIT. | Agree, similar for C_SrvN2 and C_SrvN3 SEE ANNEX DONE |
| SISCO-A17 |  | C_SrvN2 | Text in test descriptions 4,5,6 uses unknown. Note that after the server is reconfigured in step 2 the logical device, logical node and data object no longer exist. If it has to be an unknown or non-existant ObjectName any name value will satisfy the test input. | Change the text from unknown to previously known. | Agree SEE ANNEX DONE |
| SISCO-A18 |  | C_SrvN3 | Text in test descriptions 4,5,6 uses unknown. Note that after the server is reconfigured in step 2 the logical device, logical node and data object no longer exist. If it has to be an unknown or non-existant ObjectName any name value will satisfy the test input. | Change the text from unknown to previously known | Agree SEE ANNEX DONE |
| SISCO-A19 |  | C_SrvN4 | Text in test descriptions 4,5,6 uses unknown. Note that after the server is reconfigured in step 2 the logical device, logical node and data object no longer exist. If it has to be an unknown or non-existant ObjectName any name value will satisfy the test input. | Change the text from unknown to previously known | Agree SEE ANNEX DONE |
| SISCO-A20 |  | C_Ds5 | This is the only mandatory test and its not expressed in terms of 61850 services being tested. | Change to include GetDataSetValues so we know what to look for in the PIXIT Then include 4 line items in the test description, one item for each reconfiguration. | Partly agree, Added entry in PIXIT template (see annex) The client system may use a subset of the server data and datasets. As such we should remove the word “all” in the test procedures I checked for “all” in the document |
| SISCO-A21 |  | C_Ds5 | Typo in Test description 2 …. Deleta | Change to Delete a | Agree, DONE |
| SISCO-A22 |  | C_DsN1 | GetLogicalNodeDirectory(DATA-SET) is an interrogative service. Test description 5 and 6 make no sense when mapped to 8-1 (MMS GetNameList)because the client isn’t going to know what to expect in either case. | Remove Test Descriptions 5 and 6 | Agree, see Annex DONE |
| SISCO-A23 |  | C_Doc1 C_Doc2 C_Doc3 C_Doc4 C_Cnf1 C_Cnf2 C_Cnf3 C_Mdl1 C_Mdl2 C_Mdl3 | There are no detailed test or division between mandatory and optional requirements | Add additional detailed test procedures and decide which are mandatory and optional. | Results of discussion: DocX – remove “hardware” DocX – change “part 4” into IEC61850-4 PIXIT namelength is <64>/<64> only (remove the 32/32) Cnf1 – client process a subset of.. CnfX – change SCD into SCL Mdl2 – add “supported” Mdl3 – see annex DONE |
| SISCO-A24 |  | A4.2+ | We are talking about DataSets in terms of being temporary and permanent. | Globally replace temporary and permanent to non-persistent and persistent aligning with 7-2 | Agree DONE |
| SISCO-A25 |  | C_Ds7 | Expected test result is missing the numbered value | Put a 2 in front of the Expected result | Agree, DONE |
| SISCO-A26 |  | A 4.6 | The text reads Detailed test procedures for Unbuffered Reporting | Change Unbuffered to Buffered pg 60 | Agree, DONE |
| SISCO-A27 |  | C_RpN8 C_BrN8 | The meaning of detects is not strongly described | Change the abstract test case description to include The means of detection needs to specified in the PIXIT. | Agree, See annex, DONE |

| Comment Author | Clause/ Subclause | Paragraph Figure/ Table | COMMENTS | Proposed change | OBSERVATIONS OF THE Testsub comittee |
| --- | --- | --- | --- | --- | --- |
| Muschlitz 01 | A.4 | Table A.4.2 2+ | Both C_Ds7 and C_DsN5 reference “Delete Data Set” yet one is mandatory and the other is conditional | Move C_Ds7 from mandatory to conditional | Agree DONE |
| Muschlitz 02 | A.4 | Table A.4.2 4+ | C_Sg3 (GetSettingsGroupValues) is in conformance block 4 in server but is block 4+ in client | Move C_Sg3 from 4+ mandatory to block 4 conditional (see server tests) | Sg3 is conditional in 4 and mandatory in 4+ No change |
| Muschlitz 03 | A.4 | Table A.4.2 12a | C_Dons5 is missing from TimeActivatedOperate | Add C_DOns5 after “C_DOns4” | Agree, DONE |
| Muschlitz 04 | A.4 | Table A.4.2 12b | A second cancel test is needed (select OK, cancel returns response-) | Add test name after C_SBOns4 | NO, we agreed not to test cancel response- No change |
| Muschlitz 05 | A.4 | Table A.4.2 12b | SBOnsN2 is undefined | Remove SBOnsN2 from conditional column | Agree, DONE |
| Muschlitz 06 | A.4 | Table A.4.2 12b | A conditional time activated control test is needed (Select OK, TimeActivatedOperate OK, control never operates causing InformationReport- | Add test | NOT agree, SBOns does not send an information report – so there is no need to test this No change |
| Muschlitz 07 | A4.1 | C_Srv8 (Abstract) | Invalid test, 7-3 Ed1 ACT does not “originator” attribute. Perhaps there is another test which must be performed? | Remove test until Ed2 is approved | Agree, It was added based on previous comment. ACT – originator tissue #68 = ed2! DONE |
| Muschlitz 08 | A4.1 | C_SrvN2 | Description of GetAllDataValues step 6 “…with unknown data object” does not make sense because DataObject is not part of service parameters | Remove “…with unknown data object” | Agree DONE |
| Muschlitz 09 | A4.1 | C_SrvN2 | The Comment is unclear. Does this mean “some clients cannot complete this test”? Why would this be true? | Clarify | Agree, comment can be removed because the details are in the PIXIT DONE, same for SrVN3/4 |
| Muschlitz 10 | A4.1 | C_SrvN3 | Missing test: 10=”SUT requests FCDA of unknown attribute | Add test and expected result | Agree DONE |
| Muschlitz 11 | A4.1 | C_SrvN3 | The Comment is unclear. Does this mean “some clients cannot complete this test”? Why would this be true? |  | Agree, comment can be removed because the details are in the PIXIT, DONE |
| Muschlitz 12 | A4.1 | C_SrvN4 | Missing test: 10=”SUT requests FCDA of unknown attribute | Add test and expected result | Agree, DONE |
| Muschlitz 13 | A4.1 | C_SrvN4 | The Comment is unclear. Does this mean “some clients cannot complete this test”? Why would this be true? |  | Agree, comment can be removed because the details are in the PIXIT, DONE |
| Muschlitz 14 | A4.2 | C_Ds5 (Abstract) | Abstract test is unclear. What is the positive test? (How to test that “SUT checks” compared to “SUT accepts” | Editor: positive if all datasets are as expected | No change? |
| Muschlitz 15 | A4.2 | C_Ds1 | This service requires a LogicalNode to be specified | Description step 2 is missing “and logical node” at end of test | Not agree, for part 8-1 the LN is not a parameter Added a comment, DONE |
| Muschlitz 16 | A4.2 | C_Ds2 | GetDataSetDirectory does not have DATASET as a service parameter | Remove “(DATASET)” from description step 2 | Agree, DONE |
| Muschlitz 17 | A4.2 | C_Ds2 | This service requires a LogicalNode to be specified | Description step 2 is missing “and logical node” at end of test | Agree, see annex NO it just has the dataset as parameter. |
| Muschlitz 18 | A4.2 | C_Ds3 | It is unclear why test description has “(PIXIT)” | Remove the extra text | The PIXIT describes how to force the client to perform a Getdatavalues request No change |
| Muschlitz 19 | A4.2 | C_Ds4 | It is unclear why test description has “(PIXIT)” | Remove the extra text | The PIXIT describes how to force the client to perform a Setdatavalues request No change |
| Muschlitz 20 | A4.3 | C_Sub3 | This test is not needed. Client should display substituted value regardless of which client performs the substitution | Remove C_Sub3. C_Sub2 test has full test coverage | Not agree, keep as it is |
| Muschlitz 21 | A4.4 | C_Sg2 | Step “b” from abstract test description is missing | Add test step between 1 and 2 “Request GetSGCBValues …” | Agree, see Annex DONE |
| Muschlitz 22 | A4.5 | C_RpN7 (Abstract) | Typographical error “unknow”. This error appears many times in the document | Change unknow to “unknown” in whole document | Agree DONE |
| Muschlitz 23 | A4.5 | C_Rp2 | This test is very long. Perhaps it should be split into many tests? | Consider splitting the test | This reflects the way a client works. It does this all at start-up No change |
| Muschlitz 24 | A4.12 | C_Ctl1 | This test must be split into 4 parts (a…d) because different services are used | Split test | Partly agree, will specify each service for a-b-c-d, see Annex DONE |
| Muschlitz 25 | A4.12 | C_Ctl2 | This test must be split into 4 parts (a…d) because different services are used | Split test | On the certificate these tests are split for 12a/b/c/d We will keep one abstract test case and “split” the detailed detailed DONE |
| Muschlitz 26 | A4.12 | C_Ctl3 | Most servers will not allow ctlModel to be written by a client | Add note | Not agree. Similar notes are applicable for many other services, that’s why we have a PICS/PIXIT No change |
| Muschlitz 27 | A4.12 | C_CtlN1 | Select of object with ctlModel=Direct need not fail. The operate might simply clear the selection but otherwise ignore the selected state | Change expected result step 6? | Clarify the comment. Step 6 is performing a select/selectwithvalue for a direct operate DONE, clarified |
| Muschlitz 28 | A4.12 | C_CtlN1 | In test step 8, the term “non-reconfigured” is not clear | Clarify the meaning of “non-configured” control object | Remove this test step DONE |
| Muschlitz 29 | A4.12 | C_CtlN2 | I do not understand. I thought that it was a local issue how the server set ctlModel when it was unspecified in the SCD file. I would assume that SUT would read ctlModel unless the SCD specified ValKind=Conf and a specific value (otherwise, the test C_Ctl3 could not be performed because a second client would not know the previous settings from the first client to set ctlModel) | Clarify : in many SCL files the ctlModel is not initialized - the client need to resolve this to prevent intop problem. Valkind is missing in almost all SCL files | No change. |
| Muschlitz 30 | A4.12a | C_Dons (Abstract) | Missing test for TimeOperReq+ then Cancel+ | Add abstract test | A cancel after a timeoperate is not in the 7-2 ed1 figures! As such we can not test this No change |
| Muschlitz 31 | A4.12a | C_Dons (Abstract) | Missing test for TimeOperReq+ then Cancel- | Add abstract test | See before, No change |
| Muschlitz 32 | A4.12a | C_Dons | Missing detailed tests for ns3 and ns4 and ns5 | Add detailed tests | See before, No change |
| Muschlitz 33 | A4.12b | C_SBO Abstract | Missing tests: Select+, TimeOperRequest+, InformationReport- and test Select+, Cancel- | Add two abstract and detailed tests | See before, No change |
| Muschlitz 34 | A4.12c | C_DOes (Abstract) | Tests esN3 and esN4 are missing | Add abstract and detailed tests | See before, No change |
| Muschlitz 35 | A4.12d | C_SBO (Abstract) | Missing tests N3 and N4 | Add abstract and detailed tests | See before, No change |
| Muschlitz 36 | A4.12d | C_SBO (Abstract) | Missing tests for cancel of TimeActivatedOperate | Add tests | See before, No change |

| KEMA1 |  | All | To save space in tables change testcase prefix “C_” to just “c”, eg. C_SrvN1 >>> cSrvN1 |  | Agree DONE |
| --- | --- | --- | --- | --- | --- |
| KEMA2 |  | PIXIT | Check the PIXIT references in the testprocedures with the PIXIT template in Annex B |  | Agree, Done |
| TELCO |  | C_Rp8 C_Br8 C_Br11 | “all” URCB’s | Remove “all” in both abstract as detailed description | Agree DONE |
| TELCO |  |  | Action | KEMA will edit the comments into draft version 1.0 before March 24; |  |
| TELCO |  |  |  | Sisco and Bruce will review this before March 31. When OK we can approve the test procedures on the March 31 telco |  |

Annex is removed – changes are in the version 1.0 document