Migration from IEC Edition 1 to Edition 2

- Introduction to 61850

  - Edition 1 of 61850 comprised 14 parts:

    - Parts 1 to part 6

    - Part 7-1 to part 7-4

    - Part 8-1

    - Parts 9-1 and 9-2

    - Part 10

  - Edition 2 of the base specification deprecates part 9-1, revises other parts

  - Major revisions (for migration)

    - Part 6 creates a new SCL with old SCL mostly compatible

    - Part 7-1 adds statistical data, LD Hierarchies, LN inputs, testing

    - Part 7-2 adds service tracking, RBA, clarifies controls

    - Part 7-3 add many new CDCs, substitution, and a new control model

    - Part 7-4 adds many new logical nodes

    - Part 8-1 clarifies error MMS responses, file directory responses

    - Part 10 add abstract tests for clients, sampled value pub/sub, SCL

- Part 6 changes

  - New file type IID

  - New file type SED

- Part 7-1 changes

  - Logical Device Hierarchy (see 7-4 LLN0.GrRef)

  - Object names now 129 octets (64 LD + 64 DO/DA)

- Part 7-2 changes – Services

  - Modeling changes

    - New Functional Constraints

      - SR (Service Reveived)

      - OR (Operate Received)

      - BL (Blocking) {only blkEna?}

    - New basic type: INT64 (used only in CDC BCR)

  - Service Tracking

    - Added CST and CTS

    - Removed FC “CO”

  - Association

    - Role-based Access Control (Part 8-1?)

  - Setting Group

    - New control parameter: ResvTms

  - Unbuffered and buffered Reports

    - New attribute: owner

    - Clarified that if TrgOps.GI is FALSE then GI is not allowed

    - TISSUE #453 rules enforced in Edition2

  - GSSE – deprecated

  - GOOSE

    - GCB.Test is now GCB.Simulation with specific usage rules in 7-1

  - Sampled Values

    - SV.SmpSync was Boolean, now 0/1/2 (1/2=sync loca/global)

    - New SV.SmpMod

    - New SV.Simulation

  - Control Model

    - State machines changed

    - Control tracking (CTS defined in 7-2)

- Part 7-3 changes

  - New common data attributes: Cell and CalendarTime

  - New attribute in many LNs: blkEna

  - New Enumeration types: ENS, ENC, ENG

  - New CDCs

    - HST

    - VSS

    - BAC

    - ORG – includes tstEna, setSrcRef, setTstRef, intAddr, purpose

    - TSG

    - CUG

    - VSG

    - CSG

- Part 7-4 changes

  - LLN0 changes

    - LocKey – IED key switch

    - LocSta – station level switch

    - MltLev – Hierarchy of local/remote switches

    - GrRef – Hierarchy of Logical Devices

    - InRef[i] – input (source) reference

    - BlkRef[I] – dynamic blocking reference

  - LPHD changes

    - Added Sim – receive simulated GOOSE or simulated SV

  - New LNS

    - L:

      - LCCH – comm. channel

      - LGOS – GOOSE subscription

      - LSVS – Sampled Value subscription

      - LTIM – Time Management

      - LTMS – Time Master supervision

      - LTRK- service tracking

    - Q: Power Quality (many)

    - S: is now supervision of T (transducer) LNs

  - Common LN – Mod, Health, NamPlt mandatory only in “root” LLN0’s (optional in all other LNs)

  - Object order is less well-defined (part 6 example shows Mod, Beh, Health, NamPlt but part 7-4 has NamPlt, Beh, Health, Mod. Part 6 now governs order of objects within LNs

- Part 8-1 changes

  - Any takers for this?