– Conformance Statement Correction of IEC 61850-7-2:2010
(normative)

ACSI conformance statement

General

The following ACSI conformance statements shall be used to provide an overview and details about a device claiming conformance with ACSI:

–	ACSI basic conformance statement;

–	ACSI models conformance statement; and

–	ACSI service conformance statement

to specify the communication features mapped to an SCSM.

NOTE 1 The conformance statements of this annex are abstract in the sense that the ACSI models and their services are mapped to application layer models, services, and protocols. Additional details on the conformance are defined in the SCSM.

NOTE 2 For several features, the conformance requirement is implicitly defined with the common data class contained in IEC 61850-7-3 and the compatible logical-node classes and data object classes contained in IEC 61850-7-4, for example, a TrgOp (trigger option) of the value qchg (quality change) of DataAttribute requires the support of the TrgOps (trigger option) qchg of the BRCB or URCB.

ACSI basic conformance statement

The basic conformance statement shall be as defined in Table A.1.

# Table A.1 – Basic conformance statement

|  | Client/ subscriber | Server/ publisher | Value/ comments |
| --- | --- | --- | --- |
| Client-server roles |  |  |  |
| B11 | Server side (of TWO-PARTY-APPLICATION-ASSOCIATION) | – | c1 |  |
| B12 | Client side of (TWO-PARTY-APPLICATION-ASSOCIATION) | c1 | – |  |
| SCSMs supported |  |  |  |
| B21 | SCSM: IEC 61850-8-1 used |  |  |  |
| B22 | SCSM: IEC 61850-9-1 used |  |  | deprecated |
| B23 | SCSM: IEC 61850-9-2 used |  |  |  |
| B24 | SCSM: other |  |  |  |
| Generic substation event model (GSE) |  |  |  |
| B31 | Publisher side | – | O |  |
| B32 | Subscriber side | O | – |  |
| Transmission of sampled value model (SVC) |  |  |  |
| B41 | Publisher side | – | O |  |
| B42 | Subscriber side | O | – |  |
| c1 – shall be ‘M’ if support for logical-device model has been declared. O – Optional M – Mandatory |

ACSI models conformance statement

The ACSI models conformance statement shall be as defined in Table A.2.

# Table A.2 – ACSI models conformance statement

|  | Client/ subscriber | Server/ publisher | Value/ comments |
| --- | --- | --- | --- |
| If Server side (B11) and/or Client side (B12) supported |  |  |  |
| M1 | Logical device | c2 | c2 |  |
| M2 | Logical node | c3 | c3 |  |
| M3 | Data | c4 | c4 |  |
| M4 | Data set | c5 | c5 |  |
| M5 | Substitution | O | O |  |
| M6 | Setting group control | O | O |  |
|  | Reporting |  |  |  |
| M7 | Buffered report control | O | O |  |
| M7-1 | sequence-number |  |  |  |
| M7-2 | report-time-stamp |  |  |  |
| M7-3 | reason-for-inclusion |  |  |  |
| M7-4 | data-set-name |  |  |  |
| M7-5 | data-reference |  |  |  |
| M7-6 | buffer-overflow |  |  |  |
| M7-7 | entryID |  |  |  |
| M7-8 | BufTm |  |  |  |
| M7-9 | IntgPd |  |  |  |
| M7-10 | GI |  |  |  |
| M7-11 | conf-revision |  |  |  |
| M8 | Unbuffered report control | O | O |  |
| M8-1 | sequence-number |  |  |  |
| M8-2 | report-time-stamp |  |  |  |
| M8-3 | reason-for-inclusion |  |  |  |
| M8-4 | data-set-name |  |  |  |
| M8-5 | data-reference |  |  |  |
| M8-6 | BufTm |  |  |  |
| M8-7 | IntgPd |  |  |  |
| M8-8 | GI |  |  |  |
| M8-9 | conf-revision |  |  |  |
|  | Logging | O | O |  |
| M9 | Log control | O | O |  |
| M9-1 | IntgPd |  |  |  |
| M10 | Log | O | O |  |
| M11 | Control | O | M |  |
| M17 | File Transfer | O | O |  |
| M18 | Application association | M | M |  |
| M19 | GOOSE Control Block | O | O |  |
| M20 | Sampled Value Control Block | O | O |  |
| If GSE (B31/B32) is supported |  |  |  |
| M12 | GOOSE | O | O |  |
| M13 | GSSE | O | O | deprecated |
| If SVC (B41/B42) is supported |  |  |  |
| M14 | Multicast SVC | O | O |  |
| M15 | Unicast SVC | O | O |  |
| For all IEDs |
| M16 | Time | O | M | Time source with required accuracy shall be available |
| c2 – shall be ‘M’ if support for logical-node model has been declared. c3 – shall be ‘M’ if support for data model has been declared. c4 – shall be ‘M’ if support for data-set, Substitution, Report, Log Control, or Time model has been declared. c5 – shall be ‘M’ if support for Report, GSE, or SV models has been declared. M – Mandatory O – Optional |

ACSI service conformance statement

The ACSI service conformance statement shall be as defined in Table A.3 (depending on the statements in Table A.1 and in Table A.2).

Table A.3 – ACSI service conformance statement

|  | Services | AA: TP/MC | Client/ subscriber | Server/ publisher | Comments |
| --- | --- | --- | --- | --- | --- |
| Server (Clause 7) |
| S1 | GetServerDirectory (LOGICAL-DEVICE) | TP | O | M |  |
| Application association (Clause 8) |
| S2 | Associate | TP | M | M |  |
| S3 | Abort | TP | c11 | M |  |
| S4 | Release | TP | c11 | M |  |
| c11 – Either the Abort or the Release request shall be supported by the client. Additionaly, the client must understand the abort request delivered by the server. |
| Logical device (Clause 9) |
| S5 | GetLogicalDeviceDirectory | TP | O | M |  |
| Logical node (Clause 10) |
| S6 | GetLogicalNodeDirectory | TP | O | M |  |
| S7 | GetAllDataValues | TP | O | M |  |
| Data (Clause 11) |
| S8 | GetDataValues | TP | O | M |  |
| S9 | SetDataValues | TP | O | O |  |
| S10 | GetDataDirectory | TP | O | M |  |
| S11 | GetDataDefinition | TP | O | M |  |

Table A.3 (continued)

|  | Services | AA: TP/MC | Client/ subscriber | Server/ publisher | Comments |
| --- | --- | --- | --- | --- | --- |
| Data set (Clause 12) |
| S12 | GetDataSetValues | TP | O | M |  |
| S13 | SetDataSetValues | TP | O | O |  |
| S14 | CreateDataSet | TP | O | O |  |
| S15 | DeleteDataSet | TP | O | O |  |
| S16 | GetDataSetDirectory | TP | O | M |  |
|  | Services | AA: TP/MC | Client/ subscriber | Server/ publisher | Comments |
| Substitution |
| S17 | SetDataValues | TP | M | M |  |
| Setting group control (Clause 16) |
| S18 | SelectActiveSG | TP | M | M |  |
| S19 | SelectEditSG | TP | O | O |  |
| S20 | SetEditSGValue | TP | O | O |  |
| S21 | ConfirmEditSGValues | TP | O | O |  |
| S22 | GetEditSGValue | TP | O | O |  |
| S23 | GetSGCBValues | TP | O | M |  |
| Reporting (Clause 17) |
| Buffered report control block (BRCB) |
| S24 | Report | TP | c6 | c6 |  |
| S24-1 | data-change (dchg) |  |  |  |  |
| S24-2 | qchg-change (qchg) |  |  |  |  |
| S24-3 | data-update (dupd) |  |  |  |  |
| S25 | GetBRCBValues | TP | c6 | c6 |  |
| S26 | SetBRCBValues | TP | c6 | c6 |  |
| Unbuffered report control block (URCB) |
| S27 | Report | TP | c6 | c6 |  |
| S27-1 | data-change (dchg) |  |  |  |  |
| S27-2 | qchg-change (qchg) |  |  |  |  |
| S27-3 | data-update (dupd) |  |  |  |  |
| S28 | GetURCBValues | TP | c6 | c6 |  |
| S29 | SetURCBValues | TP | c6 | c6 |  |
| c6 – shall declare support for at least one (BRCB or URCB). |
| Logging (Clause 17) |
| Log control block |
| S30 | GetLCBValues | TP | M | M |  |
| S31 | SetLCBValues | TP | O | M |  |
| Log |
| S32 | QueryLogByTime | TP | c7 | M |  |
| S33 | QueryLogAfter | TP | c7 | M |  |
| S34 | GetLogStatusValues | TP | M | M |  |
| c7 – shall declare support for at least one (QueryLogByTime or QueryLogAfter). |

Table A.3 (continued)

|  | Services | AA: TP/MC | Client/ subscriber | Server/ publisher | Comments |
| --- | --- | --- | --- | --- | --- |
| Generic substation event model (GSE) |
| GOOSE (Clause 18) |
| S35 | SendGOOSEMessage | MC | c8 | c8 |  |
| GOOSE Control Block (Clause 18) |
| S36 | GetGoReference | TP | O | O |  |
| S37 | GetGOOSEElementNumber | TP | O | O |  |
| S38 | GetGoCBValues | TP | O | O |  |
| S39 | SetGoCBValues | TP | O | O |  |
| GSSE (Annex C) |
| S40 | SendGSSEMessage | MC | c8 | c8 | Deprecated |
| GSSE Control Block (Annex C) |
| S41 | GetGsReference | TP | O | O | Deprecated |
| S42 | GetGSSEDataOffset | TP | O | O | Deprecated |
| S43 | GetGsCBValues | TP | O | O | Deprecated |
| S44 | SetGsCBValues | TP | O | O | Deprecated |
| c8 – shall declare support for at least one (SendGOOSEMessage or SendGSSEMessage). c9 – shall declare support if TP association is available. |
| Transmission of sampled value model (SVC) (Clause 19) |
| Multicast SVC |
| S45 | SendMSVMessage | MC | c10 | c10 |  |
| Multicast Sampled Value Control Block |
| S46 | GetMSVCBValues | TP | O | O |  |
| S47 | SetMSVCBValues | TP | O | O |  |
| Unicast SVC |
| S48 | SendUSVMessage | TP | c10 | c10 |  |
| Unicast Sampled Value Control Block |
| S49 | GetUSVCBValues | TP | O | O |  |
| S50 | SetUSVCBValues | TP | O | O |  |
| c10 – shall declare support for at least one (SendMSVMessage or SendUSVMessage). |
| Control (Clause 20) |
| S51 | Select |  | M | O |  |
| S52 | SelectWithValue | TP | M | O |  |
| S53 | Cancel | TP | O | O |  |
| S54 | Operate | TP | M | M |  |
| S55 | Command- Termination | TP | M | O |  |
| S56 | TimeActivated-Operate | TP | O | O |  |
| File transfer (Clause 23) |
| S57 | GetFile | TP | M | M |  |
| S58 | SetFile | TP | O | O |  |
| S59 | DeleteFile | TP | O | O |  |
| S60 | GetFileAttributeValues | TP | O | M |  |
| S61 | GetServerDirectory (FILE-SYSTEM) | TP | M | M |  |

Table A.3 (continued)

|  | Services | AA: TP/MC | Client/ subscriber | Server/ publisher | Comments |
| --- | --- | --- | --- | --- | --- |
| Time (5.5) |
| T1 | Time resolution of internal clock |  |  |  | Nearest negative power of 2 in seconds |
| T2 | Time accuracy of internal clock |  |  |  | T0 |
|  |  |  |  |  | T1 |
|  |  |  |  |  | T2 |
|  |  |  |  |  | T3 |
|  |  |  |  |  | T4 |
|  |  |  |  |  | T5 |
| T3 | Supported TimeStamp resolution |  |  |  | Nearest value of 2**-n in seconds according to 6.1.2.9.3.2 |

# Conformance – Correction of IEC 61850-8-1:2011

## Notation

For the following clause, the following definitions apply.

m: mandatory support. The item shall be implemented.

c: conditional support. The item shall be implemented if the stated condition exists.

o: optional support. The implementation may decide to implement the item.

x: excluded. The implementation shall not implement this item.

i: out-of-scope. The implementation of the item is not within the scope of this standard.

F/S: Functional Standard. Should be applied.

Base: Shall be applied in any application claiming conformance to this standard.

## PICS

### Profile conformance

Table 107 and Table 108 define the basic conformance statement.

Table 107 – PICS for A-Profile support

| A-Profile shortcut | Profile Description | Client | Server | Value/comment |
| --- | --- | --- | --- | --- |
|  |  | F/S |  | F/S |  |  |
| A1 | Client/server A-Profile | c1 |  | c1 |  | Refer to 6.2 |
| A2 | GOOSE/GSE management A-Profile | c2 |  | c2 |  | Refer to 6.3 |
| A3 | GSSE A-Profile | c3 |  | c3 |  | Refer to Clause H.1 |
| A4 | TimeSync A-Profile | c4 |  | c4 |  | Refer to 6.4 |
| A5 | Security for Client/server A-Profile | o |  | o |  | Refer to IEC 62351-6 |
| A6 | Security for GOOSE/GSE management A-Profile | o |  | o |  | Refer to IEC 62351-6 |
| c1 Shall be ‘m’ if support for any service specified in Table 2 are declared within the ACSI basic conformance statement. c2 Shall be ‘m’ if support for any service specified in Table 6 are declared within the ACSI basic conformance statement. c3 Shall be ‘m’ if support for any service specified in Table H.1 are declared within the ACSI basic conformance statement. c4 Support for at least one other A-Profile shall be declared (e.g. in A1-A3) in order to claim conformance to IEC 61850-8-1. |

Table 108 – PICS for T-Profile support

| T-Profile | Profile Description | Client | Server | Value/Comment |
| --- | --- | --- | --- | --- |
|  |  | F/S |  | F/S |  |  |
| T1 | TCP/IP T-Profile | c1 |  | c1 |  | Refer to 6.2 |
| T2 | OSI T-Profile | c2 |  | c2 |  | Refer to 6.2 |
| T3 | GOOSE/GSE T-Profile | c3 |  | c3 |  | Refer to 6.3 |
| T4 | GSSE T-Profile | c4 |  | c4 |  | Refer to Clause H.1 |
| T5 | TimeSync T-Profile | o |  | o |  | Refer to 6.4 |
| c1 Shall be ‘m’ if support for A1 is declared. Otherwise, shall be 'i'. c2 Shall be ‘o’ if support for A1 is declared. Otherwise, shall be 'i'. c3 Shall be ‘m’ if support for A2 is declared. Otherwise, shall be 'i'. c4 Shall be ‘m’ if support for A3 is declared. Otherwise, shall be 'i'. |

### MMS conformance

The following conformance statements are conditional upon the support of the client/server A-Profile (e.g. A1 see profile description in Clause 6) being declared.

Except where present, MMS conformance shall be in accordance with ISO/ISP 14226-2.

#### Character sets

##### MMS identifier

The MMS Identifier shall be constrained to BasicIdentifier.

The use of ExtendedIdentifier is deprecated.

##### MMSString

The MMSString shall be constrained to use the ISO 646 String character set. All other character sets are deprecated.

##### ObjectName

The MMS ObjectName shall be constrained to use BasicIdentifier. All other character sets are deprecated.

#### Environmental services

##### Initiate conformance

Table 109 and Table 110 specify the conformance of the initiate service.

Table 109 – MMS InitiateRequest general parameters

| InitiateRequest | Client-CR | Server-CR |
| --- | --- | --- |
|  | Base | F/S | Value/range | Base | F/S | Value/range |
| InitiateRequest |  |  |  |  |  |  |
| localDetailCalling | m | m |  | M | m |  |
| proposedMaxServOutstandingCalling | m | m | 1 or greater | M | m | 1 or greater |
| proposedMaxServOustandingCalled | m | m | 1 or greater | M | m | 1 or greater |
| initRequestDetail | m | m |  | M | m |  |
| InitiateRequestDetail |  |  |  |  |  |  |
| proposedVersionNumber | m | m | Shall be 2.1 | M | m | Shall be 2.1 |
| proposedParameterCBB | m | m | See 24.2.2.2.2 | M | m | See 24.2.2.2.2 |
| servicesSupportedCalling | m | m |  | M | m |  |
| additionalSupportedCalling | c1 | x |  | c1 | x |  |
| additionalCbbSupportedCalling | c1 | x |  | c1 | x |  |
| privilegeClassIdentityCalling | c1 | x |  | c1 | x |  |
| c1 Conditional upon Parameter CBB CSPI – see Table 112. |

Table 110 – MMS InitiateResponse general parameters

| InitiateResponse | Client-CR | Server-CR |
| --- | --- | --- |
|  | Base | F/S | Value/range | Base | F/S | Value/range |
| InitiateResponse |  |  |  |  |  |  |
| localDetailCalled | m | m |  | M | m |  |
| negotiatedMaxServOutstandingCalling | m | m | 1 or greater | m | m | 1 or greater |
| negotiatedMaxServOustandingCalled | m | m | 1 or greater | m | m | 1 or greater |
| initResponseDetail | m | m |  | m | m |  |
| InitiateResponseDetail |  |  |  |  |  |  |
| negotiatedVersionNumber | m | m | Shall be 2.1 | m | m | Shall be 2.1 |
| negotiatedParameterCBB | m | m | See 24.2.2.2.2 | m | m | See 24.2.2.2.3 |
| servicesSupportedCalled | m | m | See 24.2.2.2.2 | m | m | See 24.2.2.2.2 |
| additionalSupportedCalled | c1 | x |  | c1 | x |  |
| additionalCbbSupportedCalled | c1 | x |  | c1 | x |  |
| privilegeClassIdentityCalled | c1 | x |  | c1 | x |  |
| c1 Conditional upon Parameter CBB CSPI – see Table 112. |

##### Services supported

Table 111 defines the service support requirement, and restrictions, for this standard. Relationship to ACSI services can be found in Table 1.

Table 111 – MMS service supported conformance table

| MMS service supported CBB | Client-CR | Server-CR |
| --- | --- | --- |
|  | Base | F/S | Value/range | Base | F/S | Value/range |
| initiate | o | m |  | o | m |  |
| abort | o | c15 |  | o | m |  |
| release | o | c15 |  | o | m |  |
| status | o | o |  | o | m |  |
| getNameList | o | o |  | o | c1 |  |
| identify | o | o |  | m | m |  |
| rename | o | o |  | o | o |  |
| read | o | o |  | o | c2 |  |
| write | o | o |  | o | c3 |  |
| getVariableAccessAttributes | o | o |  | o | c4 |  |
| defineNamedVariable | o | o |  | o | o |  |
| defineScatteredAccess | o | i |  | o | i |  |
| getScatteredAccessAttributes | o | i |  | o | i |  |
| deleteVariableAccess | o | o |  | o | o |  |
| defineNamedVariableList | o | o |  | o | c6 |  |
| getNamedVariableListAttributes | o | o |  | o | c5 |  |
| deleteNamedVariableList | o | o |  | o | c6 |  |
| defineNamedType | o | i |  | o | i |  |
| getNamedTypeAttributes | o | i |  | o | i |  |
| deleteNamedType | o | i |  | o | i |  |
| input | o | i |  | o | i |  |
| output | o | i |  | o | i |  |
| takeControl | o | i |  | o | i |  |
| relinquishControl | o | i |  | o | i |  |
| defineSemaphore | o | i |  | o | i |  |
| deleteSemaphore | o | i |  | o | i |  |
| reportPoolSemaphoreStatus | o | i |  | o | i |  |
| reportSemaphoreStatus | o | i |  | o | i |  |
| initiateDownloadSequence | o | i |  | o | i |  |
| downloadSegment | o | i |  | o | i |  |
| terminateDownloadSequence | o | i |  | o | i |  |
| initiateUploadSequence | o | i |  | o | i |  |
| uploadSegment | o | i |  | o | i |  |
| terminateUploadSequence | o | i |  | o | i |  |
| requestDomainDownload | o | i |  | o | i |  |
| requestDomainUpload | o | i |  | o | i |  |
| loadDomainContent | o | i |  | o | i |  |
| storeDomainContent | o | i |  | o | i |  |
| deleteDomain | o | i |  | o | i |  |
| getDomainAttributes | o | o |  | o | c14 |  |
| createProgramInvocation | o | i |  | o | i |  |
| deleteProgramInvocation | o | i |  | o | i |  |
| start | o | i |  | o | i |  |
| stop | o | i |  | o | i |  |
| resume | o | i |  | o | i |  |
| reset | o | i |  | o | i |  |
| kill | o | i |  | o | i |  |
| getProgramInvocationAttributes | o | i |  | o | i |  |
| obtainFile | o | c9 |  | o | c9 |  |
| defineEventCondition | o | i |  | o | i |  |
| deleteEventCondition | o | i |  | o | i |  |
| getEventConditionAttributes | o | i |  | o | i |  |
| reportEventConditionStatus | o | i |  | o | i |  |
| alterEventConditionMonitoring | o | i |  | o | i |  |
| triggerEvent | o | i |  | o | i |  |
| defineEventAction | o | i |  | o | i |  |
| deleteEventAction | o | i |  | o | i |  |
| alterEventEnrollment | o | i |  | o | i |  |
| reportEventEnrollmentStatus | o | i |  | o | i |  |
| getEventEnrollmentAttributes | o | i |  | o | i |  |
| acknowledgeEventNotification | o | i |  | o | i |  |
| getAlarmSummary | o | i |  | o | i |  |
| getAlarmEnrollmentSummary | o | i |  | o | i |  |
| readJournal | o | c13 |  | o | c13 |  |
| writeJournal | o | o |  | o | o |  |
| initializeJournal | o | o |  | o | c12 |  |
| reportJournalStatus | o | i |  | o | i |  |
| createJournal | o | i |  | o | i |  |
| deleteJournal | o | i |  | o | i |  |
| fileOpen | o | c8 |  | o | c8 |  |
| fileRead | o | c8 |  | o | c8 |  |
| fileClose | o | c8 |  | o | c8 |  |
| fileRename | o | i |  | o | i |  |
| fileDelete | o | c9 |  | o | c9 |  |
| fileDirectory | o | c11 |  | o | c11 |  |
| unsolicitedStatus | o | i |  | o | i |  |
| informationReport | o | c7 |  | o | c7 |  |
| eventNotification | o | i |  | o | i |  |
| attachToEventCondition | o | i |  | o | i |  |
| attachToSemaphore | o | i |  | o | i |  |
| conclude | m | m |  | m | m |  |
| cancel | o | o |  | o | m |  |
| getDataExchangeAttributes | o | c10 |  | o | c10 |  |
| exchangeData | o | c10 |  | o | c10 |  |
| defineAccessControlList | o | c10 |  | o | c10 |  |
| getAccessControlListAttributes | o | c10 |  | o | c10 |  |
| reportAccessControlledObjects | o | c10 |  | o | c10 |  |
| deleteAccessControlList | o | c10 |  | o | c10 |  |
| alterAccessControl | o | c10 |  | o | c10 |  |
| reconfigureProgramInvocation | o | c10 |  | o | c10 |  |
| c1 Shall be ‘m’ if logical device or logical node model support is declared in ACSI basic conformance statement. c2 Shall be ‘m’ if logical node model support is declared in ACSI basic conformance statement or if ACSI support for Select service or if support for the MMS write service is declared. c3 Shall be ‘m’ if ACSI support for SetDataValues, SelectActiveSG, SelectEditSG, SetEditSGValue, ConfirmEditSGValues, SetURCBValues, SetBRCBValues, SetLCBValues, SetGoCBValues, SetMSVValues, SetUMVCBValues, SelectWithValue, Cancel, Operate, or TimeActivatedOperate service is declared or implied. c4 Shall be ‘m’ if logical node model support is declared in ACSI basic conformance statement. c5 Shall be ‘m’ if data set support is declared in the ACSI basic conformance statement. c6 Shall be ‘m’ if support for defineNamedVariableList is declared. c7 Shall be 'm' if support for ACSI Report or ACSI command termination is declared. c8 Shall be 'm' if support for ACSI GetFile or SetFile is declared. c9 Shall be 'm' if support for ACSI SetFile is declared. c10 Shall not be present since MMS minor version is declared to be 1. c11 Shall be 'm' if support for ACSI GetFileAttributeValues is declared. c12 Shall be 'm' if support for the ACSI log model is declared. c13 Shall be 'm' if support for the ACSI QueryLogByTime or QueryLogAfter is declared. c14 Shall be 'm' if support for the ACSI logical device model is declared. c15 Either the Abort or the Release request shall be supported by the client. Additionaly, the client must understand the abort request delivered by the server. |

# Comments

Added for Get CB/ Set CB attributes

File transfer only applies to client / server.