Notes from UCAIug Edition 2 test procedures working group teleconference 10 January 2012 15:00 UTC:

- Review PRP/HSR test cases / test procedures

  - sPrp1/sHsr1 – there are no SCL parameters for HSR/PRP

  - sPrp1: channel A = main channel, B is always the redundant

  - Add new sPrp3 to verify incremented optional LCCH error count (FER) when channel A and B connections are reversed – Note1: this is not the case for HSR so no need to add similar test case for HSR.

  - Add a new sSrv test to verify that additional tailing bytes (PRP adds 6 bytes at the end of the packet, also security adds tailing bytes)  are accepted by the (non-PRP enabled) device

  - sHsr1 – fix the expected result numbering is 1-4-5 >> DONE

- sLogN1: the 8-1 mapping of 7-2  QueryLogAfter is confusing. Thierry will write a proposal and discuss this with the editors. The result will attached to TISSUE #809. According to MMS ReadJournal a mismatching EntryID the server will use the entryToStartAfter (timeSpecification) from the request to send the list of entries. Another issue is how to inform the client that it has missed log entries. Client could use GetLogStatusValues to verify the oldest entry in the log and compare it with the last received one.

- Topics for next telco (17 jan):

  - Review conditional/mandatory tests table A4.2

  - sGop5 – Publish GOOSE with simulation flag = T

  - sGos6 – Subscribe to GOOSE with simulation=T

  - Review conditional/mandatory tests table A4.2

  - Shall we add a sCnf testcase to verify that the valKind=Set/RO matches with the MMS read/write ability?

Richard included these notes in the draft server Ed2 test procedures document 0.6